## Slide 1: 3D Motion ControlLer
RedSox: Anundson, Chen, Ghosh, Lin, Yang

## Slide 2: Concept
Notes:   Concept in a nutshell: Manipulation of a sensor board to realistically render an image and its transitions on screen
  Rig an FPGA with sensors
  Do some math
  Realistically render a 3D image and its transitions on screen

## Slide 3: Goal and Motivation
Notes:   Gesture based control combined with 3D has many cool and interesting applications
  Interactive 3D models
  Immersive video game
  Image processing and stitching
  Render 3D environment from images and motion data

## Slide 4: Specification and Functionality
Gesture capture
  Interface with gyro and accelerometer via SPI interface
  Interpret data from the gyro and accelerometer to be used to control different demo components
    Basic control using raw gyro or accelerometer data
    Filter and combine accelerometer and gyro data into a set of orientation coordinates
2D maze to demonstrate gesture control
  Display maze
  Implement collision detection
Simple 3D rendering
  Draw a line on a VGA display between two arbitrary points
  Calculate 2D translations of corners of a cube moving in a 3D space

## Slide 5: High-Level Design 1
Gyro
Accelerometer
VGA Monitor
Switches
FPGA Design
SPI Interface
SPI Interface
VGA Driver
Orientation Calculations
orientation
acceleration
Rocking ball demo
Maze
Mode Select
Notes: Since our project is split up into 3 demos, we decided to combine demos 1 and 2 onto 1 design, and demo 3 on its own design.
Here is the FPGA design for demo 1 (rocking ball) and demo 2 (2D Maze)

## Slide 6: High-Level Design 2
Gyro
Accelerometer
VGA Monitor
FPGA Design
SPI Interface
SPI Interface
VGA Driver
Orientation Calculations
orientation
acceleration
Wireframe cube demo
Notes: Here is the FPGA design for demo 3 (3D wireframe cube)

## Slide 7
Task 1: Interface with gyro and accelerometer via SPI
Gyro and Accelerometer Interfacing Pt 1
LL, TY
Notes: Interfacing with the gyro and accelerometer: This is the first functional spec of our project. The first task of this spec is to interface with the gyro and accelerometer via the SPI interface protocol

## Slide 8
Gyro and Accelerometer Interfacing Pt 1
SPI
  Master-slave
  Master generates clock signal
  Master to slave via MOSI
  Slave to master via MISO (Full duplex)
  Slave select to “wake up” slave
LL, TY
Notes: Explanation of how SPI works

## Slide 9
ACL Interfacing
GYRO Interfacing
LL, TY
Notes: Pointing out the modules that implement the SPI interface
Master module
SPI interface module
Slave module
9

## Slide 10: Gyro and Accelerometer Interfacing Pt 2
Task 2: Combine gyro and accelerometer data into orientation using a complementary filter
http://www.instructables.com/id/PCB-Quadrotor-Brushless/step15/IMU-Part-2-Complementary-Filter/
TY
Notes: Complementary filter high-pass gyro data and low pass accelerometer data.
Gyro:the measurement has the tendency to drift, not returning to zero when the it went back to its original position. The gyroscope data is reliable only on the short term, as it starts to drift on the long term.

## Slide 11: Gyro and Accelerometer Interfacing Pt 2
LL, TY
Notes: Gyro measures the angular velocity around xyz axis.
Accelerometer measures axis’s gravity, it gives out the vector projection on gravity.

## Slide 12: Gyro and Accelerometer Interfacing Pt 2
Gyroscope
Accelerometer
CompFilter
SPI Interface Controller
SPI Interface
SPI Interface Controller
SPI Interface
16-bit xyz orientation data
TY
gyro_degree  gyro_degree+∫ gyro_data data*dt
E.g. x_degree=0.98*x_gyro+0.02*x_acc
16-bit xyz gyro data
angular velocity
10-bit xyz acc data
gravity projection
acc_degreearctan(acc_x, acc_y)
Notes: The angular velocity coming from gyro is integrated over time to get degree value and constantly added to itself.
The gravity data coming from accelerometer feeds to an arctan2 CORDIC core and spit out the degree value.
The two results are combined together with a high-pass gyro and low-pass accelerometer complimentary filter.

## Slide 13: Arbitrary Line Drawing
Bresenham’s line algorithm
  Calculates which pixels to illuminate between two points
  Can be implemented using integer math
Dual port RAM used as VGA display buffer
  Utilizes the BRAM resources in the FGPA
Module uses FIFOs to store multiple sets of line coordinates to be drawn for each screen refresh
KA

## Slide 14: Arbitrary Line Drawing
VGA Buffer
Clear Buffer
VGA Display Logic
Bresenham
Display State Machine
hcounter
vcounter
pixel_on
refresh screen
x0_coord
x1_coord
y0_coord
y1_coord
FIFO
FIFO
FIFO
FIFO
KA
Notes: Bresenham algorithm is core of line drawing module. Chooses which pixels to display.
Display state machine controls process of: clearing screen buffer, loading line points from FIFOs and writing line pixels to VGA buffer.
VGA display logic tells whether a pixel defined by hcounter and vcounter is on.

## Slide 15: Arbitrary Line Drawing
Algorithm works very well for a hardware application
  Integer math
  Simple state machine
Trade-offs
  Uses a large buffer to store screen buffer
    Design successfully implements line drawing at 640x480 resolution
    Consumes a large amount of area
    Can only store “on” or “off” so cannot store different color lines
    Possible alternatives for future development
      Use a larger FPGA device
      Use off-chip memory to store screen buffer
KA

## Slide 16: Verilog Example: Bresenham
KA
Notes: Inputs and outputs:
Clock and reset
Input points (x0,y0) and (x1,y1)
Load vals strobe initiates bresenham state machine and move it out of waiting state
Output points (x_val, y_val)
Vals_rdy flag indicates if the output values are valid
Waiting flag to indicate that the bresenham module can accept a new line to process
Parameters for widths of x and y coordinates

## Slide 17: Verilog Example: Bresenham
KA
Notes: Local parameters to define width of error and define state names
Registers for state registers, local storage of x and y coordinates for processing, registers for output flags

## Slide 18: Verilog Example: Bresenham
KA
Notes: Synchronous reset (reset current state and calculation values)
Assign default values, could be overridden by case statement
Waiting state: on load_vals strobe, load coordinates to internal registers

## Slide 19: Verilog Example: Bresenham
KA
Notes: Determine if the line is “steep” i.e. if the magnitude of the slope is greater than 1

## Slide 20: Verilog Example: Bresenham
KA
Notes: Determine if coordinates need to be swapped if slope is negative and/or steep
Take advantage of previously determined is_steep value

## Slide 21: Verilog Example: Bresenham
KA
Notes: Setup initial step and error values and intitialize x and y values used by drawing state
Draw pixel: if steep, swap x and y
increment x
calculate new error and (possibly) increment y based on error-delta_y
Repeat drawing step until reaching the end of the line

## Slide 22: Verilog Example: Bresenham
KA
Notes: Next state logic
Only states that are conditional are the waiting and drawing states

## Slide 23: Wireframe Cube Display
Functionality
  Uses Gyro And Accelerometer Data as input to manipulate 3D cube size and position
  Continually update display screen with image of cube
  Simulate matrix multiplication calculations for cube rotations in 3D space
  Values are pushed into line drawing buffer
  Use 4 fold axis rotation over
  3 or 2 fold rotation due to simplified
  calculation
KC

## Slide 24: Wireframe Cube Display
Gyro
Accelerometer
Draw Line Module
Clock
Sin & Cosine lookup table
Cube Start Coordinates
Cos & Sin of X,Y,Z
1 of 12 lines
Matrix Multiplication
broken down through incremental calculations cycles
Output Modified Coordinates
KC

## Slide 25: Wireframe Cube Display
Look up table for Values. The accuracy of values was limited to accuracy to the hundredth decimal place due to limits of the onboard memory
Insertion of Cube coordinates at starting position.
KC

## Slide 26: Wireframe Cube Display
Calculations are cascaded through a series of
Intermediate steps. This was put in due to
the limits of the FPGA. We could not squeeze in
All the calculations needed in one cycle due to
Limits in DSP48A1s Slices.
Outputs of the lookup table and coordinates are fed into the calculations
KC

## Slide 27: 2D Maze
Functionality
Takes the data input from the gyro
The VGA_Display module converts
the data to the dimensions of the ball
that moves through the maze
A 2D maze is displayed on the VGA
Collision Detection is implemented by the inputs taken from the gyro
The aim of the game is to move the ball to the end of the maze
AG, KA, LL

## Slide 28: 2D Maze
Features of the Maze
A switch is provided which
when turned on enables the
maze to blink.
Different portions of the maze appear
at regular intervals hence making it
tougher for the ball to complete the game
The color of the maze keeps changing throughout the game giving it a visual appeal.
AG, KA, LL

## Slide 29: 2D Maze Game
Top
Accelerometer
32-bit xyz orientation data
task3
VGA Controller
Maze and Ball Logic
Maze Portion Files
Ball Logic
Cursor ROM (Baseball sprite)
Gyro
Accelerometer
VGA Monitor
Switches
Data Select
SPI Component
AG, KA, LL

## Slide 30: 2D Maze Game
Verilog Code Snippet showing the Maze Display
AG, KA, LL

## Slide 31: 2D Maze Game
Verilog Code Showing Collision Detection
AG, KA, LL
Notes: Abby

## Slide 32: Project Reflections: Successes and Future Work Pt 1
Gyro + ACL Interfacing
  Interfacing was relatively simple, since the SPI interface code was already written
  Would have been nice to write SPI interface modules (Or some custom protocol..?)
Complimentary Filter
  Data scaling is tricky
  More accurate (expensive) pmod components would be better
  Could write SPI interface ourselves and use wider sensing range
Line Drawing (Bresenham’s)
  Might be nice to store screen buffer off-chip (Latency issues)
  Possibly use larger FPGA so screen buffer does not consumer all BRAM resources

## Slide 33: Project Reflections: Successes and Future Work Pt 2
2D Maze
  Successfully integrating the Maze and the movement of the ball with the Gyro on one board.
  Would have been better to have implemented the 3D Maze, although it requires more memory
Wireframe Cube
  Memory and limits in calculation blocks were a constant ceiling we kept hitting. Need a beefier board.
  Initial concept was to form a cube. But realized it would have been more interesting to draw insides of a room and used gyro to “look around” the room
  Timing errors in calculations were not caught by the program and as a result gave a lot of misleading readings that required many hours of debugging
Notes: 2D Maze
Wireframe Cube

## Slide 34: Questions?